## Slide 1
OVPM Co-Design Toolkit · Tool 52 of 133
Method canvas for co-design
Temporary urbanism prototype
What this tool produces · A low-cost, short-term physical alteration of a public space (e.g., a pop-up parklet, a painted pedestrian plaza) accompanied by data on how the community naturally uses the new configuration.
G2 · Proof of Fit
Dimensions
Spatial
Social / User
With simplexity

## Slide 2
TOOL 52 · FACILITATOR PREPARATION
Preparing the workshop · Temporary urbanism prototype
G2 · Proof of Fit
Why this tool matters
Breaking the paralysis of long-term planning through immediate action; proving to skeptical residents that a hostile asphalt intersection can become a welcoming human square overnight.
Evidence we produce
A low-cost, short-term physical alteration of a public space (e.g., a pop-up parklet, a painted pedestrian plaza) accompanied by data on how the community naturally uses the new configuration.
Duration & Material
Duration · 1 week for installation, 1 to 3 months of temporary testing and observation Material · Paint, modular seating, mobile greenery, observation grids, user feedback surveys
Reference case
The PopUpUrbanSpaces project across Central Europe utilized tactical urbanism to reclaim streets. In Varaždin (Croatia), a street redesign prototype was tested with temporary materials. Follow-up measurements recorded an asphalt temperature drop from 50°C to 30°C, and on-site surveys confirmed a 95% public approval rate, accelerating the city's commitment to permanent pedestrian-oriented interventions.
Suggested agenda · Brief (10 min) › Method walk-through (15 min) › Animation canvas (60–90 min) › Harvest (20 min)
With simplexity

## Slide 3
TOOL 52 · ANIMATION CANVAS · TEMPORARY URBANISM PROTOTYPE
Quick · cheap · reversible · learn
Duration
1 week for installation, 1 to 3 months of temporary tes…
Quick
days, not months
Cheap
low-cost materials
Reversible
can be removed
Measurable
data-driven learning
Instrumentation · what we measure
Footfall
Dwell time
Use mix
Sentiment
Income / cost
With simplexity

## Slide 4
TOOL 52 · HARVEST
Harvesting our learnings
After running the canvas, capture three layers of insight.
Stand-out signals, surprising stories, ideas to remember
Concrete adaptations to our context, our team, our constraints
Skills, allies, resources, decisions still to secure
What inspires me
How to apply it here
What we need to be autonomous
Each participant fills a copy. Then debrief together to surface patterns and next steps.
With simplexity