## Slide 1
OVPM Co-Design Toolkit · Tool 106 of 133
Method canvas for co-design
Carbon footprint & GHG accounting
What this tool produces · A Baseline Emission Inventory (BEI) documenting the tonnes of CO2-equivalent generated across municipal operations, transport, waste, and local industry.
G1 · Proof of Impact
G4 · Proof of Sustainability
Dimensions
Environmental
Economic
Regulation
With simplexity

## Slide 2
TOOL 106 · FACILITATOR PREPARATION
Preparing the workshop · Carbon footprint & GHG accounting
G1 · Proof of Impact
Why this tool matters
Making the city administratively accountable for the global atmosphere, translating the daily mechanics of turning on lights and driving cars into a shared metric of planetary responsibility.
Evidence we produce
A Baseline Emission Inventory (BEI) documenting the tonnes of CO2-equivalent generated across municipal operations, transport, waste, and local industry.
Duration & Material
Duration · 2 to 4 months for data collection and calculation Material · Local utility billing data, municipal fleet records, standardized GHG emission factor tables (e.g., Covenant of Mayors guidelines)
Reference case
Thousands of local authorities participating in the EU Covenant of Mayors rely on compiling a rigorous Baseline Emission Inventory (BEI) as the mandatory first step of their Sustainable Energy and Climate Action Plans (SECAP). By systematically tracking emissions from buildings, transport, and waste, cities like Barcelona establish clear data-driven targets to cut GHG emissions by 2030, ensuring subsequent interventions are measurable and accountable.
Suggested agenda · Brief (10 min) › Method walk-through (15 min) › Animation canvas (60–90 min) › Harvest (20 min)
With simplexity

## Slide 3
TOOL 106 · ANIMATION CANVAS · CARBON FOOTPRINT & GHG ACCOUNTING
GHG inventory · scopes 1 · 2 · 3
Duration
2 to 4 months for data collection and calculation
Scope 1
direct emissions fleet · boilers · processes
Scope 2
electricity & district heat purchased
Scope 3
indirect chain · upstream + downstream goods · travel · waste · investments
Scope 3 typically dominates · do not skip it.
With simplexity

## Slide 4
TOOL 106 · HARVEST
Harvesting our learnings
After running the canvas, capture three layers of insight.
Stand-out signals, surprising stories, ideas to remember
Concrete adaptations to our context, our team, our constraints
Skills, allies, resources, decisions still to secure
What inspires me
How to apply it here
What we need to be autonomous
Each participant fills a copy. Then debrief together to surface patterns and next steps.
With simplexity